## Slide 1: Linux Device Drivers
Roman Okhrimenko 2019
Lection 2

## Slide 2: Questions to answer on this lection
1. What is Linux Device Tree?
2. Another language?
3. Device Tree files syntax overview
4. I2C and USB bus based drivers implementation overview - similar?
5. Autodetecting and issues with it, Udev rules
6. Industrial I/O subsystem overview
7. IIO subsystem interface example

## Slide 3: What is Linux Device Tree
It is new approach to describing hardware that is actually present in system.
A way to isolate hardware description from kernel image.
OS independent thus widely portable between different systems.
Describes device information in a system that cannot be dynamically detected by a client program.
Effective with corresponding drivers that support Device Tree bindings

## Slide 4: Another language
Device Tree uses special language to implement concept.
Files extensions are .dts (source) and .dtsi (includes) – C style
Device Tree files need to be compiled to a binaries with Device Tree Compiler.
Binary files extensions .dtbo
Folder to search for Device Tree files /arch/arm/boot/dts
/arch/arm/boot/dts/overlays

## Slide 5: Device Tree files Syntax overview
Thomas Petazzoni – Device Tree for Dummies

## Slide 6: Device Tree files examples

## Slide 7: I2C, SPI and USB bus based drivers
I2C, SPI bmp085 pressure sensor example
*core.c file to implement bmp085 sensor functionality
*-i2c.c file to implement binding to I2C bus in system
*-spi.c file to implement binding to SPI bus in system

## Slide 8: I2C, SPI and USB bus based drivers

## Slide 9: I2C, SPI and USB bus based drivers
bmp280_spi_probe() {… return bmp280_common_probe(&spi->dev, …));}
bmp280_spi_remove() {…}
bmp280_spi_read() {…}
bmp280_spi_write() {…}
bmp280-spi.c
bmp280_i2c_probe() {… return bmp280_common_probe(&client->dev, …));}
bmp280_i2c_remove() {…}
bmp280_i2c_read() {…}
bmp280_i2c_write() {…}
bmp280-i2c.c
bmp280_common_probe() {… implementation for device …}
bmp280_common_remove() {…}
struct iio_dev population <- bme280_chip_info
iio channels description
methods registered to chip info implementation
bmp280-core.c

## Slide 10: I2C, SPI and USB bus based drivers
STM32Leds USB bus char device driver
- register device to USB bus subsystem
implement usb_class_driver device interface requirements
use USB API calls in read/write/open/release

## Slide 11: Autodetecting and issues with it
Refer to
https://github.com/romanjoe/os-course-labs/tree/master/usb

## Slide 12: Industrial I/O subsystem overview
kernel framework to support functional requirements of typical sensors using mostly I2C and SPI buses
used with devices with higher updates rate > 100KHz

## Slide 13: Industrial I/O subsystem overview
Industrial IO subsystem
stack overview
https://wiki.st.com/stm32mpu/wiki/IIO_overview

## Slide 14: IIO Subsystem
Continuing with bmp280 driver code

## Slide 15: Industrial I/O Subsystem
Continuing with bmp280 driver code
same as for k-attributes in sysfs
with special macro helper
dedicated IIO info structure
dedicated IIO device structure

## Slide 16: References
https://bootlin.com/pub/conferences/2013/elce/petazzoni-device-tree-dummies/petazzoni-device-tree-dummies.pdf
https://static.lwn.net/images/pdf/LDD3/ch13.pdf
https://elinux.org/images/5/53/10-Years-of-the-Industrial-IO-Kernel-Subsystem-Jonathan-Cameron-Huawei.pdf
http://reactivated.net/writing_udev_rules.html
https://wiki.st.com/stm32mpu/wiki/IIO_overview
https://youtu.be/NDXYpR_m1CU - Linux kernel debugging tools and approaches